## Slide 1: CG2111A
Studio 15
TCP/IP + TLS

## Slide 2: TCP / IP vs 7-Layer
OSI 7-Layer Model
TCP/IP Model
Process-to-process data transfer
Routing of datagrams from host to host
bits on the transmission media
data transfer between neighbouring network elements

## Slide 3: TCP / IP : In Action
Source: Partially from Wikipedia

## Slide 4: TCP – Transmission Control Protocol
IP is a “best effort” protocol
Additional check and controls are needed for reliable end-to-end communication
TCP ensures:
  Packets are sent and acknowledged
  Packets are reassembled in correct order
  A “connection” is established between the sender / receiver
  Etc……

## Slide 6: Socket Programming
An API built on TCP/IP
Socket
Server
Port
Transport
Internet
Network Access
Socket
Client
Transport
Internet
Network Access
Port

## Slide 7: So……
alex-server.cpp
Server (Alex’s PI)
Port
alex-client.cpp
Client (Your Laptop)
Port
Transport
Internet
Network Access
Transport
Internet
Network Access

## Slide 8: Transport Layer Security

## Slide 9: The General Idea
Encryption Process consists of:
Plaintext
Algorithm
Key
Text (Information) to be encrypted
A series of steps used to encrypt the text
Special information used by the algorithm for encryption
Only holder of key can decrypt the information later

## Slide 10: Encryption Process: Illustration
k nqxf aqw
Key
I love you
Plaintext
Encryption
Algorithm
Ciphertext

## Slide 11: Decryption Process: Illustration
Key
k nqxf aqw
Ciphertext
Encryption
Algorithm
I love you
Plaintext

## Slide 12: The problem of key distribution
Distribution of key is still the weakest link
  To securely send information by encryption, you need to first tell recipient about the key in secured way
In the age of Internet, this is even more important!
  Need to send information through an unsecured medium
Solving the key distribution problem is the most significant breakthrough in encryption

## Slide 13: The key distribution problem: Illustration
Scenario:
  Alice and Bob need to communication securely
  Eve is trying to eavesdrop
There is no way for Alice and Bob to agree on an encryption key without Eve knowing
Alice
Bob
Eve
Bob, the key is “computing”
Aha! Got you!

## Slide 14: Some background
Key to encrypt and decrypt is the same
  known as symmetric key encryption
  hence the key cannot be compromised
The breakthrough discovery: asymmetrical key encryption
  Use different keys to encrypt and decrypt
Public Key Encryption is one such example
  Uses public key to encrypt
  Uses private key to decrypt

## Slide 15: Public Key Encryption: Basic Idea
The public key and private key must be related mathematically
  It should be hard to deduce the private key from public key
Public key is widely publicized
  used to encrypt message only
  cannot decrypt encrypted message
Private key should be kept secret
  used to decrypt message only

## Slide 16: Public Key Encryption: Illustration
Alice
Bob
Eve
Bob, my public key is “CEG”
private key = rocks
ok
ok
Alice
Bob
Eve
private key = rocks
KXWYALO…
argh! cannot decrypt using “CEG”

## Slide 17: Public and Private Key: Is it possible?
The idea of public key encryption is suggested before anyone know how to find such keys
  Many consider such thing to be impossible
Two teams eventually solve the problem:
  James Ellis, Clifford Cocks and Malcolm Williamson (1975)
    Government Communications Headquarters (England)
  Ronald Rivest, Adi Shamir and Leonard Adleman (1978)
    Massachusetts Institute of Technology (USA)
The algorithm is known as RSA after the 2nd team
  Why not the 1st team?

## Slide 18: Public and Private Key: Basic Idea
Instead of covering the full algorithm, we show the basic idea behind the generation of public and private key
To generate a public key:
  Choose two prime numbers p and q
  Calculate N = p x q
  N is the public key, while p and q form the private key
Given N, it is very hard to discover the p and q
  i.e. through the process of factorization

## Slide 19: Factorization: Is it hard?
At first look, it seems easy to deduce p and q from N
Try the following:
  N = 143 p = _______ q = __________
  N = 8633 p = _______ q = __________
  N = 175, 828, 273 p = _______ q = __________
In actual usage, N is typically in the range of 21024
Remember, RSA is not unbreakable, just “unbreakable in reasonable time” 

## Slide 20: Diffie-Hellman-Merkle Key Exchange
One use of the public-private key idea is:
  Exchange a symmetric key for both party to use
  Once key is successfully exchanged, normal symmetric encryption/decryption can be used

## Slide 21: Diffie-Hellman-Merkle Key Exchange

## Slide 22: Are you Alice?
Alice
Bob
Eve
Bob, my public key is “computing”
Bob, I am the real Alice, my public key is “fun”
I’m so confused!

## Slide 23: Check my signature
encryptpublic_key( M )  N
decryptprivate_key( N )  M
Reverse is also true!
encryptprivate_key ( M )  N
decryptpublic_key ( N )  M

## Slide 24: Are you Alice - Solution
Alice
Bob
Bob, my public key is “computing”
private key = rocks
Message M
Message M
Alice my public key is “engineering”
private key = funz
DigestA
DigestA
DigestB
DigestA
DigestA
Message M
DigestA
Message M
DigestA

## Slide 25: Are you Alice - Is it really solved?
Alice
Bob
Bob, my public key is “computing”
private key = rocks
Message M
Message M
Alice my public key is “engineering”
private key = funz
DigestA
DigestA
DigestB
DigestA
DigestA
Message M
DigestA
Message M
DigestA

## Slide 26: Introducing Charlie
Alice
Bob
Bob, my public key is “computing”
private key = rocks
Alice my public key is “engineering”
private key = funz
PublicKeyA
Digest
Charlie
private key = soconfused
Everyone, my public key is “trustworthy”
PublicKeyA
Digest

## Slide 28: W9S2 – In a nutshell
Cert. Signing Authority
signing.key
(public key)
Digest
signing.pem
Alex's Pi
alex.key
(Public Key)
signing.pem
signing.key
X.csr (Certificate Request)
X.crt
(Certificate)
alex.csr
(Certificate Request)
alex.crt
(Certificate)
signing.pem
A1
A2.1.1
A2.1.4
Operator Laptop
laptop.key
(Public Key)
laptop.csr
(Certificate Request)
A2.2.1
laptop.crt
(Certificate)
signing.pem
A2.1.4
A3
(basic TLS)
A4
(TLS+Ctrl)

## Slide 29: Handout Updates
Step 1.1 Generating The CA Key
openssl genrsa –des3 –out signing.key 4096
tls-alex-server.cpp
Locate the line #define BAUD_RATE B57600 Change to: #define BAUD_RATE B9600